#
# $Id: ser.cfg,v 1.25.2.1 2005/02/18 14:30:44 andrei Exp $
#
# simple quick-start config script
#

# ----------- global configuration parameters ------------------------

debug=3 # debug level (cmd line: -dddddddddd)
#fork=yes
#log_stderror=no	# (cmd line: -E)

# Uncomment these lines to enter debugging mode
#fork=no
#log_stderror=yes

check_via=no	# (cmd. line: -v)
dns=no # (cmd. line: -r)
rev_dns=no # (cmd. line: -R)

listen=10.128.1.52
port=5060
children=4

fifo="/tmp/ser_fifo"

# ------------------ module loading ----------------------------------

# Uncomment this if you want to use SQL database
#loadmodule "/usr/local/lib/ser/modules/mysql.so"

loadmodule "/usr/local/lib/ser/modules/sl.so"
loadmodule "/usr/local/lib/ser/modules/tm.so"
loadmodule "/usr/local/lib/ser/modules/rr.so"
loadmodule "/usr/local/lib/ser/modules/maxfwd.so"
loadmodule "/usr/local/lib/ser/modules/usrloc.so"
loadmodule "/usr/local/lib/ser/modules/registrar.so"
loadmodule "/usr/local/lib/ser/modules/textops.so"

# Uncomment this if you want digest authentication
# mysql.so must be loaded !
#loadmodule "/usr/local/lib/ser/modules/auth.so"
#loadmodule "/usr/local/lib/ser/modules/auth_db.so"

# ----------------- setting module-specific parameters ---------------

# -- usrloc params --

modparam("usrloc", "db_mode", 0)

# Uncomment this if you want to use SQL database
# for persistent storage and comment the previous line
#modparam("usrloc", "db_mode", 2)

# -- auth params --
# Uncomment if you are using auth module
#
#modparam("auth_db", "calculate_ha1", yes)
#
# If you set "calculate_ha1" parameter to yes (which true in this config),
# uncomment also the following parameter)
#
#modparam("auth_db", "password_column", "password")

# -- rr params --
# add value to ;lr param to make some broken UAs happy
modparam("rr", "enable_full_lr", 1)

#add mediaproxy for NAT transversal --- Mike
modparam("mediaproxy","mediaproxy_select","/var/run/proxydispatcher.sock")

# ------------------------- request routing logic -------------------

# main routing logic

route{

# initial sanity checks -- messages with
# max_forwards==0, or excessively long requests
if (!mf_process_maxfwd_header("10")) {
sl_send_reply("483","Too Many Hops");
break;
};
if (msg:len >= 2048 ) {
sl_send_reply("513", "Message too big");
break;
};

# we record-route all messages -- to make sure that
# subsequent messages will go through our proxy; that's
# particularly good if upstream and downstream entities
# use different transport protocol
if (!method=="REGISTER") record_route();

# subsequent messages withing a dialog should take the
# path determined by record-routing
if (loose_route()) {
# mark routing logic in request
append_hf("P-hint: rr-enforced\r\n");
route(1);
break;
};

if (!uri==myself) {
# mark routing logic in request
append_hf("P-hint: outbound\r\n");
route(1);
break;
};

# if the request is for other domain use UsrLoc
# (in case, it does not work, use the following command
# with proper names and addresses in it)
if (uri==myself) {

if (method=="REGISTER") {

# Uncomment this if you want to use digest authentication
#	if (!www_authorize("iptel.org", "subscriber")) {
#	www_challenge("iptel.org", "0");
#	break;
#	};

save("location");
break;
};

lookup("aliases");
if (!uri==myself) {
append_hf("P-hint: outbound alias\r\n");
route(1);
break;
};

# native SIP destinations are handled using our USRLOC DB
if (!lookup("location")) {
sl_send_reply("404", "Not Found");
break;
};
};
append_hf("P-hint: usrloc applied\r\n");
route(1);
}

route[1]
{
# send it out now; use stateful forwarding as it works reliably
# even for UDP2TCP
if (!t_relay()) {
sl_reply_error();
};
}